## Slide 1
<Insert Picture Here>
16 3D Support
Solids, Point Clouds, Tins

## Slide 2: Agenda
Concepts
Using the Z
  3D Coordinate Systems
Modeling 3D Objects
  3D Queries
  From 2D to 3D: Extrusions
  Publishing 3D objects: cityGML, KML
Point Clouds and Tins
  Data models
  Loading and clipping

## Slide 3: What does 3D support cover ?
Using the Z
  3D Coordinate systems
Modeling 3D objects
  Points, lines, polygons with Z
  Surfaces and solids
Capturing the reality
  New specialized types
  Point clouds resulting from laser scanning
  Triangulated surfaces (TINs)

## Slide 4
<Insert Picture Here>
3D Coordinate Systems

## Slide 5: 2D Coordinate Systems
There are two kinds of 2D systems:
Geographic 2D
  Example: SRID 4326 (Longitude/Latitude WGS 84)
Projected 2D
  Example: SRID 27700 (OSGB 1936 / British National Grid)

## Slide 6: 3D Coordinate Systems
There are two kinds of 3D systems:
Geographic 3D
  Based on longitude and latitude, plus ellipsoidal height
  The ellipsoidal height is the height relative to a reference ellipsoid, which is an approximation of the real Earth
  Example: SRID 4327 (Longitude/Latitude WGS84 3D)
Compound Systems
  Based on a geographic or projected two-dimensional system, plus gravity-related height
  Example: SRID 7405 (OSGB36 / British National Grid + ODN)
  Combines SRID 27700 (horizontal 2D projection) and SRID 5701 (vertical component)

## Slide 7: Vertical Systems
Gravity-related height : the height as influenced by the Earth's gravitational force, where the base height (zero) is an equipotential surface
The height of any point is an approximation of its distance above or below "sea level“
Example: SRID 5701 (Ordnance Datum Newlyn)
Based on Mean Sea Level at Newlyn (Cornwall) between 1915 and 1921.

## Slide 8: Getting Information about 3D systems
Must search the full data model.
Table SDO_COORD_REF_SYSTEM (actually a view)
select srid, coord_ref_sys_name,coord_ref_sys_kind
from sdo_coord_ref_system
where srid in (4326, 4327, 27700, 5701, 7405);
SRID COORD_REF_SYS_NAME COORD_REF_SYS_KIND
----- ------------------------------------- ------------------
4326 WGS 84 GEOGRAPHIC2D
4327 WGS 84 (geographic 3D) GEOGRAPHIC3D
5701 Newlyn VERTICAL
7405 OSGB36 / British National Grid + ODN COMPOUND
27700 OSGB 1936 / British National Grid PROJECTED
5 rows selected.

## Slide 9: How is a Compound System Formed ?
select coord_ref_sys_name, cmpd_horiz_srid, cmpd_vert_srid
from sdo_coord_ref_system
where srid = 7405;
COORD_REF_SYS_NAME CMPD_HORIZ_SRID CMPD_VERT_SRID
---------------------------------------- --------------- --------------
OSGB36 / British National Grid + ODN 27700 5701
1 row selected.

## Slide 10: Creating a New Compound System
insert into sdo_coord_ref_system (
srid, coord_ref_sys_name, coord_ref_sys_kind,
cmpd_horiz_srid, cmpd_vert_srid, is_legacy
)
values (
314685783,
'DHDN / Gauss-Kruger zone 4 + DHHN92 height',
'COMPOUND',
31468,
5783,
’FALSE'
);
commit;

## Slide 11: Conversions: 2D <-> 3D
SDO_CS.MAKE_3D(geometry, Z, srid)
  Adds the specified Z value for each vertex (0 if not specified)
  Use the specified 3D SRID for the result (or keep original 2D SRID)
SDO_CS.MAKE_2D(geometry, srid)
  Removes all Z from the geometry
  Use the specified 2D SRID for the result (or keep original SRID)
Applies only to simple 3D shapes
  Points, lines, polygons (= simple surfaces = faces)

## Slide 12
<Insert Picture Here>
Migrating from Earlier Release

## Slide 13: Validating 2½D structures
In 11.2.0.2 and 11.2.0.3: geometries must have a 3D SRID !
Apply patch 10296467 (VALID GEOMETRY IS CONSIDERED INVALID WHEN USING COMPOUND CS)
Or validate in 2D:
Or use the “10g compatibility” mode:
Specific 3D rules applied
ORA-54668: a 2D SRID cannot be used with a 3D geometry
SDO_GEOM.VALIDATE_GEOMETRY_WITH_CONTEXT (
SDO_CS.MAKE_2D(geometry), 0.05
)
SDO_GEOM.VALIDATE_GEOMETRY_WITH_CONTEXT (
geometry, 0.05, NULL, ‘TRUE’
)
Use 10g rules (ignore 3D)

## Slide 14: Validating 2½D structures
Arcs are not allowed !
Lines: points with same X and Y but different Z are no longer considered as duplicates !
Simple Surfaces: must be planar !
3D validation is more expensive (CPU)
Specific 3D rules applied

## Slide 15: Remove Unnecessary Z values
Data that is not really 3D
  Shapes with Z set to 0 or NULL
  Common for data imported from CAD systems
Horizontal shapes
  Lines or polygons with all Z identical
  Are the Z really used by the application ?
Convert them to 2D with SDO_CS.MAKE_2D(geometry)
  Removes the Z values

## Slide 16: Queries on 2½D data
Now performed using 3D rules!
Two 2 ½ lines with different Z no longer intersect !
3D queries are much slower than 2D queries
  No internal optimizations!
Use 2D spatial index
  Will now use 2D rules for queries (Z are ignored)
  This is the default!

## Slide 17
<Insert Picture Here>
3D Data Structures

## Slide 18: Exploiting the Z in “classic” geometries
Point
  X, Y, Z
Line
  Suite of points X,Y,Z
Polygon = Simple Surface = Face
  All points must be in the same plane
  A simple surface can have any polygonal shape (possibly with voids)
  Only straight lines or rectangles (no arcs or circles)
  Any orientation
    But holes must have the opposite orientation to the outer ring

## Slide 19: SDO_GEOMETRY – Classic Types
Object Type | GTYPE | ETYPE | Content
Point | 3001 | 1 | One point X,Y,Z
Line | 3002 | 2 | One line (suite of X,Y,Z) Z can be different
Polygon ( = simple surface) | 3003 | 1003 2003 | One planar polygon (X,Y,Z), possibly with holes
Multi Point | 3005 |  | Several points
Multi Line | 3006 |  | Several lines
Multi Polygon | 3007 | 1003 2003 | Several disjoint planar polygons (can be in different planes)

## Slide 20: Modeling Surfaces
Simple Surface = Polygon = face
  All points are in the same 3D plane.
Composite Surface
  Formed by multiple connected faces
  Must form a single continuous area
  Can be open or closed
  Faces cannot intersect
  Adjacent faces must be in different planes (*)
Example: the surface of a cube is a composite surface:
  Formed by 6 connected faces
  Each face is a square
This surface does not form a solid
  Just like a closed line does not form a polygon
(*) this rule is optional

## Slide 21: SDO_GEOMETRY – Composite Surfaces
Object Type | GTYPE | ETYPE | Content
Composite Surface | 3003 | 1x1006 Nx1003 | One or more connected planar polygons forming a single continuous area Element types: 1x1006 (composite surface) indicating the number N of simple surfaces that form the composite. Then Nx1003 (one per simple surface)
Multi Composite Surface | 3007 | Nx1006 Nx1003 | One or more disconnected composite surfaces. Element types: Nx1006 (composite surface) each followed by 1003’s.

## Slide 22: Example of Composite Surface
Y
Z
X
(4,6,0)
(4,1,4)
SDO_GEOMETRY (
3003, -- 3-dimensional surface,
NULL,
NULL,
SDO_ELEM_INFO_ARRAY (
1, -- starting offset,
1006, -- composite surface
2, -- 2 simple surfaces
1,1003,3, -- first surface rectangle
7,1003,3 -- second surface rectangle
),
SDO_ORDINATE_ARRAY(
2,1,0, 4,6,0, 2,1,0, 4,1,4
)
)
(2,1,0)

## Slide 23: Optimized Surfaces
3D Box
Aligned with coordinate axes
Specify only “bottom lower left” and “upper top right” points
Z
Y
X

## Slide 24: Modeling Solids
Simple Solid
  Formed by a single external closed surface
  Can also have one or more internal surfaces, forming holes in the solid
  Holes cannot touch external surfaces
  Faces must not have holes
  A cube or a pyramid are examples of simple solid
Composite Solid
  Formed by N connected simple solids
  Could also be a simple solid delimited by a composite surface
  Must form a single continuous volume

## Slide 25: SDO_GEOMETRY - Solids
Object Type | GTYPE | ETYPE | Interpretation / Content
Simple Solid | 3008 | 1x1007 Nx1006 | One simple solid Element types: 1x1007 (simple solid) indicating the number N of surfaces (1006) that form the solid. Then Nx1006 (one per surface)
Box Solid | 3008 | 1x1007 | Box aligned with coordinate axes min (x,y,z) and max (x,y,z)
Composite Solid | 3008 | 1x1008 Nx1007 | N connected simple solids, forming a single continuous volume
Multi-Solid | 3009 | Nx1008 or Nx1007 | N disconnected simple or composite solids.

## Slide 26: Example of Simple Solid
SDO_GEOMETRY:
3008 – 3-dimensional solid,
SRID,
NULL,
SDO_ELEM_INFO_ARRAY (
1 - starting offset,
1007 - solid element
1 - one surface,
1, 1006, 6 - 1 ext surface w 6 faces
1, 1003, 1 - First face
…
n, 1003, 1 - Last face
),
SDO_ORDINATE_ARRAY(
-- ordinate specification for each face
a, b, d, c, a,
e, d, b, h, e,
…
a, c, f, g, a
)
)
Z
Y
X
a
b
c
d
e
f
g
h
Maximum Complexity of a 3D Object
Each point is 3D (x,y,z)
Maximum capacity is 349525 points
Up to 87381 triangular faces
Each point (e.g. “a”) is three ordinates (e.g. Xa, Ya, Za)

## Slide 27: Face orientation rules
Z
Y
X
a
b
c
d
e
f
g
h
Based on the surface normal of each face
The order of the vertices implicitly defines the surface normal using the “right-hand thumb” rule
If the fingers curl along the order of the specification of the vertices, the outward thumb is the direction of the surface normal for the polygon.

## Slide 28: Example of Optimized Solid : Box
SDO_GEOMETRY (
3008 – 3-dimensional solid,
SRID,
NULL,
SDO_ELEM_INFO_ARRAY (
1 - starting offset,
1007 - solid element
3 - Axis-aligned box,
),
SDO_ORDINATE_ARRAY(
2,2,0, - first endpoint
4,4,2 - second endpoint
)
)
(2,2,0)
(4,4,2)
Z
Y
X

## Slide 29: Example of Solid with Hole
Hole:
(aH,bH,…hH)
Z
Y
X
a
b
c
d
e
f
g
h
SDO_GEOMETRY (
3008 – 3-dimensional solid,
SRID,
NULL,
SDO_ELEM_INFO_ARRAY (
1, 1007, 1 - solid element
1, 1006, 6 - 1 exterior surface (formed
by 6 simple surfaces)
1, 1003, 1 – 6 simple surfaces
…
n, 2006, 6 - 1 interior surface
n, 1003, 1 – 6 simple surfaces
…
),
SDO_ORDINATE_ARRAY(
ordinate specification for:
-- each face of exterior surface (abdc,..),
-- each face of interior surface
(aHcHdHbH,…)
)
)

## Slide 30: Example: Building with Atrium Modeled as a composite solid
Model as a composite solid formed from four simple solids:
A (north wing)
D (south wing)
B (west wing)
C (east wing)
Y
Z
X
A
C
D
B

## Slide 31: Example: Building with Atrium Modeled as a composite solid
SDO_GEOMETRY (
3008 – 3-dimensional solid,
SRID,
NULL,
SDO_ELEM_INFO_ARRAY (
1, 1008, 4 - composite solid (formed by 4
simple solids)
1, 1007, 1 - First solid
1, 1006, 6 - Cmp surf (6 simple surfaces)
1, 1003, 1 - 6 simple surfaces
…
n, 1007, 1 – last solid
n, 1006, 6 - Cmp surf (6 simple surfaces)
n, 1003, 1 – 6 simple surfaces
…
),
SDO_ORDINATE_ARRAY(
ordinate specification for each face of
each solid
)
)
Z
X
A
C
D
B

## Slide 32: Example: Building with Atrium Modeled as a simple solid
Can also model as a simple solid with a single composite surface.
Cannot represent top and bottom faces as polygons with holes.
Represent it as a simple solid with multiple faces:
  Four top faces: a, b, c, d
  Four side faces: e (front), f (right), g (back) and h (left)
  Four bottom faces: i, j, k, l
Could also represent top and bottom surfaces as (ab) and (cd) or (abc) and (d)
Z
Y
X
a
c
d
b
e
f
Z
Y
X
e
f
ab
cd

## Slide 33: Example: Building with Atrium Modeled as a simple solid
Z
Y
X
a
c
d
b
e
f
SDO_GEOMETRY (
3008 – 3-dimensional solid,
SRID,
NULL,
SDO_ELEM_INFO_ARRAY (
1, 1007, 1 - solid element
1, 1006,16 - 1 exterior surface (formed
by 16 simple surfaces)
1, 1003, 1 – 1st simple surface
…
n, 1003, 1 – last simple surface
),
SDO_ORDINATE_ARRAY(
ordinate specification for each face
(a, b, c, d)
(e, f, g, h)
…
)
)

## Slide 34: Validating 3D structures
Arcs are not allowed
Lines: points with same X and Y but different Z are no longer considered as duplicates
Simple Surfaces: must be planar
Composite surfaces: simple surfaces must connect and be in different planes
Surfaces in solids must be correctly oriented
  Different rules than 2D polygons
Surfaces cannot intersect
  A hole in a solid must not touch any of the other surfaces
Specific 3D rules applied

## Slide 35: Validating 3D structures
CONDITIONAL
  Applies to composite surfaces (or solids)
  Applies to adjacent faces in the same plane
  When TRUE (the default) then this case is not allowed
  When FALSE, this case is accepted
FLAG10G
  Applies to 3D points, lines and polygons
  When TRUE, validation is done on 2D rules (Z are ignored)
  When FALSE (the default) validation is one on 3D rules
VALIDATE_GEOMETRY_WITH_CONTEXT
RETURNS VARCHAR2
Argument Name Type
--------------- --------------
THEGEOMETRY SDO_GEOMETRY
TOLERANCE NUMBER
CONDITIONAL VARCHAR2
FLAG10G VARCHAR2
ORA-54516: adjacent outer rings of composite surface cannot be on same plane

## Slide 36: Summary of 3D GTYPES
Object Type | GTYPE | Content
Point | 3001 | One 3D point
Line | 3002 | One 3D line
Surface | 3003 | One 3D surface (simple or composite)
Solid | 3008 | One 3D solid (simple or composite)
Multi Point | 3005 | Several points
Multi Line | 3006 | Several lines
Multi Surface | 3007 | Several surfaces
Multi Solid | 3009 | Several solids
Collection | 3004 | Any combination of 3D objects

## Slide 37: Spatial 3D Data Model
Hierarchical Decomposition
Composite Solid
Simple Solid
Composite Surface
Face
Line
Point
Multi Solid
Ring

## Slide 38
<Insert Picture Here>
Operations on 3D Data

## Slide 39: Operations on 3D Data
Spatial indexing in 3D
  3D Rtrees
Spatial queries
  SDO_FILTER
  SDO_ANYINTERACT, SDO_INSIDE, SDO_CONTAINS
  SDO_WITHIN_DISTANCE
  SDO_NN
Measurements
  Distance
  Length
  Area
  Volume
Generate 3D shapes
  Convert 2D polygons to 3D solids (by extrusion)
Publish
  Extract 3D objects to KML and GML
Load
  Load 3D objects from GML
Process
  Extract components of a 3D geometry.
  Solids, composite surfaces in each solid, simple surfaces, etc
Validate
  Verify the validity of a 3D object

## Slide 40: From 2D to 3D: Extrusion
Transform 2D polygons (building footprints) to 3D solids
Use the SDO_UTIL.EXTRUDE() function
  Pass the 2D polygon as input
  Pass the height of the solid
  Pass the ground height
The result is a 3D solid
The function attempts to use the 3D SRID that corresponds to the input 2D SRID
  Sets it to NULL if it finds no correspondance

## Slide 41: Extrusion Syntax
GEOMETRY:
  2D polygon to extrude
  Must be a polygon without arcs but can have holes
GRDHEIGHT:
  Ground height for each vertex of the polygon
  Pass just one value if all vertices share the same ground height
HEIGHT:
  Height for each vertex of the polygon
  Pass just one value if all vertices share the same height
TOL:
  Tolerance to use
OPTIONAL3DSRID:
  Three-dimensional coordinate system (SRID) to be assigned to the returned geometry. If you do not specify this parameter, Spatial automatically assigns a three-dimensional SRID value based on the SRID value of the input geometry.
FUNCTION EXTRUDE
RETURNS SDO_GEOMETRY
Argument Name Type
--------------- ----------------
GEOMETRY SDO_GEOMETRY
GRDHEIGHT SDO_NUMBER_ARRAY
HEIGHT SDO_NUMBER_ARRAY
TOL NUMBER
OPTIONAL3DSRID NUMBER
Height
Ground height

## Slide 42: Extrusion example
select sdo_util.extrude (
sdo_geometry(2003, null, null,
sdo_elem_info_array (1,1003,3),
sdo_ordinate_array (2,2, 4,4)
),
sdo_number_array(0),
sdo_number_array(2),
0.05
)
from dual;
(2,2)
(4,4)
Y
X
Z
Y
X
SDO_GEOMETRY (
3008, NULL, NULL,
SDO_ELEM_INFO_ARRAY(
1, 1007, 1, -- One simple solid
1, 1006, 6, -- One composite surface (6 faces)
1, 1003, 1, -- face 1
16, 1003, 1, -- face 2
31, 1003, 1, -- face 3
46, 1003, 1, -- face 4
61, 1003, 1, -- face 5
76, 1003, 1 -- face 6
),
SDO_ORDINATE_ARRAY(
2,4,0, 4,4,0, 4,2,0, 2,2,0, 2,4,0,
2,4,2, 2,2,2, 4,2,2, 4,4,2, 2,4,2,
2,4,0, 2,2,0, 2,2,2, 2,4,2, 2,4,0,
2,2,0, 4,2,0, 4,2,2, 2,2,2, 2,2,0,
4,2,0, 4,4,0, 4,4,2, 4,2,2, 4,2,0,
4,4,0, 2,4,0, 2,4,2, 4,4,2, 4,4,0
)
)

## Slide 43: Extrusion example
SDO_GEOMETRY(
3008, NULL, NULL,
SDO_ELEM_INFO_ARRAY(
1, 1008, 2, -- Composite solid (formed by 2 solids)
1, 1007, 1, -- First solid
1, 1006, 11, -- Composite surface (11 faces)
1, 1003, 1,
31, 1003, 1,
61, 1003, 1,
76, 1003, 1,
91, 1003, 1,
106, 1003, 1,
121, 1003, 1,
136, 1003, 1,
151, 1003, 1,
166, 1003, 1,
181, 1003, 1,
196, 1007, 1, -- Second solid
196, 1006, 7, -- Composite surface (7 faces)
196, 1003, 1,
214, 1003, 1,
232, 1003, 1,
247, 1003, 1,
262, 1003, 1,
277, 1003, 1,
292, 1003, 1
),
SDO_ORDINATE_ARRAY (
4,2,0, 4,3,0, 4,4,0, 3,4,0, 3,3,0, 2,3,0, 2,5,0, 5,5,0, 5,2,0, 4,2,0,
4,2,2, 5,2,2, 5,5,2, 2,5,2, 2,3,2, 3,3,2, 3,4,2, 4,4,2, 4,3,2, 4,2,2,
…
3,3,0, 3,3,2, 4,3,2, 4,3,0, 3,3,0, 2,3,0, 2,3,2, 3,3,2, 3,3,0
)
)
select sdo_util.extrude (
sdo_geometry(2003, null, null,
sdo_elem_info_array (1,1003,3, 5,2003,3),
sdo_ordinate_array (2,2, 5,5, 3,3, 4,4)
),
sdo_number_array(0),
sdo_number_array(2),
0.05
)
from dual;
Y
X
Z
Y
X

## Slide 44: Decomposing a 3D object: EXTRACT3D
GEOMETRY:
  3D object to extract from
LABEL:
  Specifies the component to extract.
  A string of up to 7 comma-separated numbers
  Each component of a 3D object has a unique label
FUNCTION EXTRACT3D
RETURNS SDO_GEOMETRY
Argument Name Type
--------------- ----------------
GEOMETRY SDO_GEOMETRY
LABEL VARCHAR2
Composite Solid
Simple Solid
Composite Surface
Face
Edge
Point
Multi Solid
Ring

## Slide 45: Element Labels
Labels are strings of up to 7 comma-separated numbers
Each number identifies a component at a level of decomposition
P, E, R, F, S, V, M
M | Number of a solid in a multi-solid.
V | Number of a solid in a composite solid
S | Number of a composite surface in a simple solid
F | Number of a face in a composite surface
R | Number of a ring in a face
E | Number of a edge (line) in a ring
P | Number of point in an edge
Composite Solid
Simple Solid
Composite Surface
Face
Edge
Point
Multi Solid
Ring

## Slide 46: Examples of Labels
Composite Solid
Gtype is 3008. Etype is 1008 (composite solid) followed by 4x1007 (solids)
Solid A: ‘0,0,0,0,0,1’
Solid B: ‘0,0,0,0,0,2’
Composite surface of solid B: ‘0,0,0,0,1,2’
Faces of solid B: ‘0,0,0,1,1,2’ to ‘0,0,0,6,1,2’
Simple Solid
Gtype is 3008. Etype is 1007 (solid) followed by 1006 (composite surface) and 6x1003 (faces)
Composite surface of solid A: ‘0,0,0,0,1’
Faces of solid B: ‘0,0,0,1,1,’ to ‘0,0,0,6,1’
A
A
C
D
B

## Slide 47: Examples of Labels
Multi-Solid
Gtype is 3009. Etype is 1007 with 1006, then another 1007
Solid A: ‘0,0,0,0,0,0,1’
Solid B: ‘0,0,0,0,0,0,2’
Composite surface of solid B: ‘0,0,0,0,1,1,2’
Faces of solid B: ‘0,0,0,1,1,1,2’ to ‘0,0,0,6,1,1,2’
B
A
Composite Surface
Gtype is 3003. Etype is 1006 followed by 2x1003
Face A: ‘0,0,0,1’
Face B: ‘0,0,0,2’
B
A

## Slide 48
<Insert Picture Here>
Publishing and Viewing
CityGML, KML

## Slide 49: Convert to KML
Use the SDO_UTIL.TO_KMLGEOMETRY() function
Must use 11.1.0.7 or later !
select sdo_util.to_kmlgeometry(
sdo_util.extrude (
sdo_geometry(2003, null, null,
sdo_elem_info_array (1,1003,3, 5,2003,3),
sdo_ordinate_array (2,2, 5,5, 3,3, 4,4)
),
sdo_number_array(0),
sdo_number_array(2),
0.05
)
)
from dual;

## Slide 50: Raw KML output
<MultiGeometry>
<Polygon>
<extrude>0</extrude><tessellate>0</tessellate><altitudeMode>relativeToGround</altitudeMode>
<outerBoundaryIs>
<LinearRing>
<coordinates>
4.0,2.0,0.0 4.0,3.0,0.0 4.0,4.0,0.0 3.0,4.0,0.0 3.0,3.0,0.0 2.0,3.0,0.0 2.0,5.0,0.0
5.0,5.0,0.0 5.0,2.0,0.0 4.0,2.0,0.0
</coordinates>
</LinearRing>
</outerBoundaryIs>
</Polygon>
<Polygon>
<extrude>0</extrude><tessellate>0</tessellate><altitudeMode>relativeToGround</altitudeMode>
<outerBoundaryIs>
<LinearRing>
<coordinates>
4.0,2.0,2.0 5.0,2.0,2.0 5.0,5.0,2.0 2.0,5.0,2.0 2.0,3.0,2.0 3.0,3.0,2.0 3.0,4.0,2.0
4.0,4.0,2.0 4.0,3.0,2.0 4.0,2.0,2.0
</coordinates>
</LinearRing>
</outerBoundaryIs>
</Polygon>
...
</MultiGeometry>

## Slide 51: Generate KML documents
Use the XML facilities of the Oracle database
Then publish to XDB repository
Must convert to WGS84 (4327) if your data is projected
SELECT xmlelement ( "kml",
xmlattributes ('http://www.opengis.net/kml/2.2' as "xmlns"),
xmlelement ("Document",
xmlagg (
xmlelement ("Placemark",
xmlelement ("name", 'Building '|| gmlid),
xmltype (
sdo_util.to_kmlgeometry (sdo_cs.transform(geom,4327))
)
)
)
)
)
FROM buildings_ext;

## Slide 52: Enable Access to XDB repository
Access to XDB repository is disabled by default
  HTTP and FTP ports set to “0”
Check the current XDB port settings
Set HTTP and FTP Ports for XDB to standard ports
Create a folder for the KML files
select dbms_xdb.gethttpport as "HTTP-Port", dbms_xdb.getftpport as "FTP-Port"
from dual;
exec dbms_xdb.setHTTPPort(8090);
exec dbms_xdb.setFTPPort(21);
declare
result boolean;
begin
result := dbms_xdb.createFolder('/public/Buildings');
end;
/

## Slide 53: Publish KML in the XDB Repository
declare
result boolean;
kmldoc xmltype;
begin
SELECT xmlelement ( "kml",
xmlattributes ('http://www.opengis.net/kml/2.2' as "xmlns"),
xmlelement ("Document",
xmlelement ("Style",
xmlattributes('BuildingStyle' as "id"),
xmlelement ("LineStyle", xmlelement ("width",'1'),xmlelement ("color“,'ff0000ff')),
xmlelement ("PolyStyle", xmlelement ("color", '7d0000ff'))
),
xmlagg (
xmlelement ("Placemark",
xmlelement ("name", 'Building '|| gmlid),
xmlelement ("styleUrl", '#BuildingStyle'),
xmltype (
sdo_util.to_kmlgeometry (snap_to_ground (sdo_cs.transform(geom,4327),0))
)
)
)
)
)
INTO kmldoc
FROM buildings_ext;
result := dbms_xdb.createResource ('/public/Buildings/buildings_ext.kml', kmldoc);
end;
/
Style definition
Use the style
Fix Z values
Transform to WGS84

## Slide 54: Access the KML files
FTP
HTTP
WebDAV

## Slide 55: View in Google Earth
Define a network link to the kml file
Specify URL to the KML document in the Oracle XDB repository

## Slide 56
View in Google Earth

## Slide 57: Convert to GML
Use the SDO_UTIL.TO_GML311GEOMETRY() function
select sdo_util.to_gml311geometry(
sdo_util.extrude (
sdo_geometry(2003, null, null,
sdo_elem_info_array (1,1003,3, 5,2003,3),
sdo_ordinate_array (2,2, 5,5, 3,3, 4,4)
),
sdo_number_array(0),
sdo_number_array(2),
0.05
)
)
from dual;

## Slide 58: Raw GML output
<gml:CompositeSolid srsName="SDO:" xmlns:gml="http://www.opengis.net/gml">
<gml:solidMember>
<gml:Solid>
<gml:exterior>
<gml:CompositeSurface>
<gml:surfaceMember>
<gml:Polygon>
<gml:exterior>
<gml:LinearRing>
<gml:posList srsDimension="3">
4.0 2.0 0.0 ... 4.0 2.0 0.0
</gml:posList>
</gml:LinearRing>
</gml:exterior>
</gml:Polygon>
</gml:surfaceMember>
<gml:surfaceMember><gml:Polygon> ... </gml:Polygon></gml:surfaceMember>
...
<gml:surfaceMember><gml:Polygon> ... </gml:Polygon></gml:surfaceMember>
</gml:CompositeSurface>
</gml:exterior>
</gml:Solid>
</gml:solidMember>
<gml:solidMember><gml:Solid> ... </gml:Solid></gml:solidMember>
</gml:CompositeSolid>

## Slide 59: Convert to CityGML
Use the XML facilities of the Oracle database
Then publish to XDB repository
SELECT xmlelement(
"CityModel",
xmlattributes(
'http://www.citygml.org/citygml/1/0/0' as "xmlns",
'http://www.opengis.net/gml' as "xmlns:gml",
'http://www.w3.org/1999/xlink' as "xmlns:xlink",
'http://www.w3.org/2001/XMLSchema-instance' as "xmlns:xsi“,
'http://www.citygml.org/citygml/1/0/0/CityGML.xsd' as "xsi:schemaLocation"
),
xmlagg (
xmlelement ("cityObjectMember",
xmlelement("GenericCityObject",
xmltype ( sdo_util.to_gml311geometry(geom) ) as "lod1Geometry"
)
)
)
)
as CityGML
FROM buildings_ext;

## Slide 60: Publish GML in the XDB Repository
declare
result boolean;
gmldoc xmltype;
begin
SELECT xmlelement( "CityModel",
xmlattributes(
'http://www.citygml.org/citygml/1/0/0' as "xmlns",
'http://www.opengis.net/gml' as "xmlns:gml",
'http://www.w3.org/1999/xlink' as "xmlns:xlink",
'http://www.w3.org/2001/XMLSchema-instance' as "xmlns:xsi",
'http://www.citygml.org/citygml/1/0/0/CityGML.xsd' as "xsi:schemaLocation"
),
xmlagg (
xmlelement ("cityObjectMember",
xmlelement("GenericCityObject",
xmltype ( sdo_util.to_gml311geometry(geom) ) as "lod1Geometry"
)
)
)
)
INTO gmldoc
FROM buildings_ext;
result := dbms_xdb.createResource ('/public/Buildings/buildings_ext.xml', gmldoc);
end;
/

## Slide 61: Access the XML files
FTP
HTTP
WebDAV

## Slide 62
<Insert Picture Here>
Loading 3D data

## Slide 63: Loading CityGML
Use the Java example program CGMLToSDO.java
Provided in $ORACLE_HOME/md/demo/CityGML/examples
Parses a CityGML file
Loads the objects into a table
set CLASSPATH=.;%ORACLE_HOME%/jdbc/lib/ojdbc5.jar; %ORACLE_HOME%/lib/xmlparserv2.jar;%ORACLE_HOME%/md/jlib/sdoapi.jar;%ORACLE_HOME%/md/jlib/sdoutl.jar
java SdoLoadCityGML -host 127.0.0.1 -port 1521 -sid orcl111 -user scott -password tiger -file CityGML_British_Ordnance_Survey.xml -table buildings -geomcol geom -featurecol feature -idcol building_id -srid 7405

## Slide 64: Data Models for City Landscapes
Structures at multiple levels of detail
Textures and facades
Orthophotos
Versioning
LOD1 Building
Blocks without roof structures
LOD2 Building
Full roof structures, possibly with textures
LOD3 Building
Detailed architecture
LOD4 Building
Interior structures
http://www.3dcitydb.net/
Illustrations courtesy of Technical University Berlin - Institute for Geodesy and Geoinformation Science

## Slide 65: Semantic City Models
Geometries
  Shape, location, topology
  3D structures (solids, faces, …)
Appearance
  Textures, levels of detail
Semantics
  Meaning and function of the objects
  Also part or objects
Queries combine geometry and semantics
Thematic display considering semantics
Multi-criteria analysis
More than just visualization of reality
Illustrations courtesy of Technical University Berlin - Institute for Geodesy and Geoinformation Science

## Slide 66
<Insert Picture Here>
Querying 3D Data

## Slide 67: Populate 3D metadata
SQL> INSERT INTO USER_SDO_GEOM_METADATA
2> (TABLE_NAME, COLUMN_NAME, DIMINFO, SRID)
3> VALUES (
4> 'BUILDINGS',
5> 'GEOM',
6> SDO_DIM_ARRAY (
7> SDO_DIM_ELEMENT ('Easting', 0, 1000000, 0.05),
8> SDO_DIM_ELEMENT ('Northing', 0, 1000000, 0.05),
9> SDO_DIM_ELEMENT ('Elevation', 0, 1000, 0.05)
10> ),
11> 27700
12> );

## Slide 68: Creating a 3D index
Must specify explicitly
If not specified, you get a 2D index
  The metadata must still be 3D!
SQL> CREATE INDEX buildings_sx ON buildings (geom)
2> INDEXTYPE IS MDSYS.SPATIAL_INDEX
3> PARAMETERS ('sdo_indx_dims=3');
SQL> CREATE INDEX buildings_sx ON buildings (geom)
2> INDEXTYPE IS MDSYS.SPATIAL_INDEX;

## Slide 69: Some 3D queries
Find the building interacting with a 3D point
SELECT building_id, (height - ground_height) height
FROM buildings_ext
WHERE SDO_ANYINTERACT (
geom,
SDO_GEOMETRY (
3001, 7405,
SDO_POINT_TYPE (442249, 111480, 8),
NULL,NULL
)
) = 'TRUE';

## Slide 70: Some 3D queries
Find the building interacting with a 3D point
Point is in WGS84 (GPS) coordinates
SELECT building_id, (height - ground_height) height
FROM buildings_ext
WHERE SDO_ANYINTERACT (
geom,
SDO_GEOMETRY (
3001, 4327,
SDO_POINT_TYPE (-1.400562, 50.9012567, 55.0693992),
NULL,NULL
)
) = 'TRUE';

## Slide 71: Some 3D queries
Find all buildings less than 50 meters from one specific building
SELECT b1.building_id,
SDO_GEOM.SDO_DISTANCE (
b1.geom, b2.geom, 0.05) distance,
(b1.height - b1.ground_height) height
FROM buildings_ext b1,
buildings_ext b2
WHERE SDO_WITHIN_DISTANCE (
b1.geom, b2.geom, 'distance=50 unit=m'
) = 'TRUE'
AND b2.building_id = 42
ORDER BY distance;

## Slide 72: Some 3D queries
Get the building closest to one selected building, and that is over 2 meters taller
SELECT b1.building_id,
(b1.height - b1.ground_height) height
FROM buildings_ext b1,
buildings_ext b2
WHERE SDO_NN (b1.geom, b2.geom) = 'TRUE'
AND b2.building_id = 42
AND (b1.height-b1.ground_height) –
(b2.height-b2.ground_height) > 2
AND ROWNUM <= 1;

## Slide 73: Combining 2D and 3D
Query 3D data using a 2D window
Example:
  Find all (3D) pipeline sections that cross a (2D) land parcel
Query 2D data using a 3D window
Example:
  Find all (2D) land parcels on the path of a (3D) pipeline section

## Slide 74: Combining 2D and 3D Summary of Capabilities
Data | Index | Window | 
 |  | 2D | 3D
2D | 2D | 2D Query | 2D Query (Z are ignored)
3D | 2D | 2D Query (Z are ignored) | 
 | 3D | 3D Query with Z forced to 0 | 3D Query

## Slide 75: Java Interface
Class J3D_Geometry
Subtype of JGeometry
Some methods :
  Validate (tolerance): Returns true or false
  Distance (J3D_geometry): Returns distance
  Anyinteract (J3D_Geometry): Returns true or false
  Length(): returns the length of a line geometry
  Area(): returns area for a surface geometry
  Volume(): returns volume of a solid geometry
Classe ElementExtractor
  Extract and iterate on all components of a J3D_Geometry
  Solids, composite surfaces in each solid, simple surfaces, etc.

## Slide 76
<Insert Picture Here>
Point Clouds

## Slide 77: What is LiDAR Data ?
Collection performed by:
  Airplanes, helicopters or drones
  Ground vehicles
  Underwater vehicles
  Fixed stations
Sensors collect millions of 3D points per second, along with attributes
Results are scenes formed of billions of points (“point clouds”)
Laser Imaging Detection and Ranging

## Slide 78: Point Cloud Challenges
Data Volumes
  increasing densities with technology – Billions of points
  Multi-return 150 KHz * 4 = 600k/sec
  Full-waveform 250 KHz * 2048 =512,000,000/sec
Storage
  Where do I put all this data ?
  Archive? Security ? Compress?
  Optimal format for analysis? LAS, LAZ, CSV, Proprietary
Analysis
  Derivative product generation (TINs, Contours, DEMs)
  Correlate with other data (vector, raster, networks, addresses …)

## Slide 79: Storage Model (1): using the SDO_PC type
Separates logical from physical structures
Logical structures
  Tables containing an SDO_PC column
  Contains generic attributes and footprint
  Also contains a pointer to a PC block table
Physical structures
  “Block tables”
  Contain point cloud blocks
  Can be very large
  Structure defined in SDO_PC_BLK object type

## Slide 80: Storage Model
Logical structures
Contains point cloud metadata and footprint
Also contains a pointers to one or more block tables
Physical structures
Point cloud block tables
Contain the points
Can be very large
Could be partitioned
Add new tables as necessary
pc 1
pc 2
pc 3
pc 4
pc 5
pc 6
pc 1 blocks
pc 2 blocks
pc 3 blocks
pc 4 blocks
pc 5 blocks
pc 6 blocks

## Slide 81: Storage Model
pc 1
pc 2
pc 3
pc 4
PC table
pc 1 blocks
pc 2 blocks
PC blocks table 1
pc 3 blocks
pc 4 blocks
pc 5 blocks
pc 6 blocks
pc 5
pc 6
PC blocks table 2

## Slide 82: Storage Model
pc 1
pc 2
pc 3
pc 4
PC table 1
pc 1 blocks
pc 2 blocks
PC blocks table
pc 3 blocks
pc 4 blocks
pc 5 blocks
pc 6 blocks
pc 5
pc 6
PC table 2

## Slide 83: Package SDO_PC_PKG
Initialization of a « point cloud »
  sdo_pc_pkg.init()
Loading a point cloud from a set of point objects
  sdo_pc_pkg.create_pc()
Extracting points in a spatial window
  sdo_pc_pkg.clip_pc()
Converting to SDO_GEOMETRY
  sdo_pc_pkg. to_geometry()

## Slide 84: Point Clouds Workflow using SDO_PC
Point Cloud tables
Direct load from LAS files
Flat files
Flat files
LiDAR files
LiDAR loader
Point tables
LiDAR Files
Point loader
LiDAR Files
Flat Files
Load flat ASCII files into point tables …
… then build the point cloud from the point tables
Build from point tables
Query and Clip
Convert to Geometries
Generate Elevation Contour Lines

## Slide 85: Loading Point Clouds in SDO_PC
Input: Files in ASPRS LAS binary format (« LAS files »)
Option 1: Direct Loading
  Use commercial tools (FME etc)
  Use open source libLAS tools and libraries (« las2oci »)
Option 2: Loading via text formats
  Convert LAS files to text flat files (« las2txt »)
  Load text files into a simple point table (sql*loader)
  Create point cloud from the point table

## Slide 86: 1. Creating Point Cloud Tables
Use the SDO_PC type
Can have any number of PC tables
Include any combination of attributes
Scenes can be searched on any attribute
Also the spatial extent of the scene
CREATE TABLE LIDAR_SCENES(
ID NUMBER PRIMARY KEY,
COLLECTION_TS TIMESTAMP,
DESCRIPTION CLOB,
... (any number of attributes) ...
POINT_CLOUD SDO_PC
);

## Slide 87: The SDO_PC type
PC_EXTENT is the footprint of the point cloud
Needs a spatial index to support spatial searching
BASE_TABLE VARCHAR2(70)
BASE_TABLE_COL VARCHAR2(1024)
PC_ID NUMBER
BLK_TABLE VARCHAR2(70)
PTN_PARAMS VARCHAR2(1024)
PC_EXTENT MDSYS.SDO_GEOMETRY
PC_TOL NUMBER
PC_TOT_DIMENSIONS NUMBER
PC_DOMAIN MDSYS.SDO_ORGSCL_TYPE
PC_VAL_ATTR_TABLES MDSYS.SDO_STRING_ARRAY
PC_OTHER_ATTRS SYS.XMLTYPE
PC table and column
Block table and column

## Slide 88: The SDO_PC type
Attribute | Explanation
BASE_TABLE | Name of the base table containing a column of type SDO_PC
BASE_TABLE_COL | Name of the column of type SDO_PC in the base table
PC_ID | ID number for the point cloud
BLK_TABLE | Name of the table that contains information about each block in the point cloud.
PTN_PARAMS | Parameters for partitioning the point cloud
PC_EXTENT | SDO_GEOMETRY object representing the spatial extent of the point cloud (the minimum bounding object enclosing all objects in the point cloud)
PC_TOL | Tolerance value for points in the point cloud.
PC_TOT_DIMENSIONS | Total number of dimensions in the point cloud. Includes spatial dimensions and any nonspatial dimensions, up to a maximum total of 9.
PC_DOMAINS | (Not currently used.)
PC_VAL_ATTR_TABLES | SDO_STRING_ARRAY object specifying the names of any value attribute tables for the point cloud
PC_OTHER_ATTRS | XMLTYPE object specifying any other attributes of the point cloud

## Slide 89: 2. Creating Point Cloud Block Tables
Using the SDO_PC_BLK type
Define a primary key on the object and block ids
Use SECUREFILE lobs (new structure in 11g)
Allows compression of the LOBs!
  (also encryption and de-duplication)
CREATE TABLE PC_BLK_01 OF SDO_PC_BLK (
PRIMARY KEY (
OBJ_ID, BLK_ID
)
)
LOB(POINTS) STORE AS SECUREFILE
(COMPRESS HIGH NOCACHE NOLOGGING);

## Slide 90: The SDO_PC_BLK type
Describes one block of points
Contains the unique identifier of the block
  Scene id (OBJ_ID, same as PC_ID) and block id (BLK_ID)
OBJ_ID NUMBER
BLK_ID NUMBER
BLK_EXTENT MDSYS.SDO_GEOMETRY
BLK_DOMAIN MDSYS.SDO_ORGSCL_TYPE
PCBLK_MIN_RES NUMBER
PCBLK_MAX_RES NUMBER
NUM_POINTS NUMBER
NUM_UNSORTED_POINTS NUMBER
PT_SORT_DIM NUMBER
POINTS BLOB

## Slide 91: The SDO_PC_BLK type
Attribute | Explanation
OBJ_ID | ID number of the point cloud object
BLK_ID | ID number of the block.
BLK_EXTENT | Spatial extent of the block.
BLK_DOMAIN | (Not currently used.)
PCBLK_MIN_RES | Minimum resolution level at which the block is visible in a query. The block is retrieved only if the query window intersects the spatial extent of the block and if the minimum - maximum resolution interval of the query. Usually, lower values mean farther from the view point, and higher values mean closer to the view point.
PCBLK_MAX_RES | Maximum resolution level at which the block is visible in a query.
NUM_POINTS | Total number of points in the POINTS BLOB
NUM_UNSORTED_POINTS | Number of unsorted points in the POINTS BLOB
PT_SORT_DIM | Number of the dimension (1 for the first dimension, 2 for the second dimension, etc) on which the points are sorted.
POINTS | BLOB containing the points.

## Slide 92: PC BLOB Structure
The BLOB contains an array of points
Each point encoded as
  d 64-bit floating point numbers (d = the dimensionality of the point)
  One 32 bit integer representing the point number
  One 32 bit integer representing the partition (= block) number
Future: compressed format
  Storing coordinates as offsets from the origin of the block MBR
  Using short integers

## Slide 93: 3. Loading using libLAS
Available from http://liblas.org/
For Windows, download and install pre-build binaries in the OSGeo4W package http://trac.osgeo.org/osgeo4w/
  A packaging of a number of open source tools: libraries, desktop GIS (Quantum, Grass, …), servers (UMN Mapserver, …)
Main tools (see http://liblas.org/docs.html for details)
  lasinfo = returns information about a LAS file
  las2oci = loads a LAS file into Oracle
  las2las = copy and transform a LAS file
  las2txt = converts a LAS file to a text format
  txt2las = the reverse
NOTES
liblas needs gdal 1.8 to be installed

## Slide 94: Using las2oci
las2oci --verbose --input Serpent_Mound_Model_LAS_Data.las
--connection scott/tiger@orcl112
--base-table-name LIDAR_SCENES --cloud-column-name POINT_CLOUD
--block-table-name PC_BLK_01 --block-capacity 10000
--srid 32617
--input | Path to the input LAS file
--connection scott/tiger@orcl112 | Database connection
--base-table-name LIDAR_SCENES | Name of point cloud table
--cloud-column-name POINT_CLOUD | Name of point cloud column
--block-table-name PC_BLK_01 | Name of the block table
--block-capacity 10000 | Points per block
--srid 32617 | Coordinate system of the point cloud

## Slide 95: Using las2oci
If the block table does not exist, it will be created automatically
  Better to create it yourself beforehand
The point cloud table must contain a column called ID
  Automatically numbered
Many parameters available
  « las2oci --help» or see http://liblas.org/utilities/las2oci.html
  Filter and transform input
  Apply pre and post SQL
NOTE: las2oci loads only the X,Y,Z, Intensity and Time dimensions

## Slide 96: 4. Loading from text files
The input is a comma-separated-values (csv) file structure
You can create one from a las file using las2txt
Can choose the format of the output (precision, separator, content)
Can apply various filters and transformations
las2txt –i Serpent_Mound_Model_LAS_Data.las
-o Serpent_Mound_Model_LAS_Data.dat -v
289814.15,4320978.61,170.76
289814.64,4320978.84,170.76
289815.12,4320979.06,170.75
289815.60,4320979.28,170.74
...

## Slide 97: Use all dimensions
Specify the dimensions to include
M specifies a point sequence number
Note that the SDO_PC type only allows 9 dimensions.
las2txt –input Serpent_Mound_Model_LAS_Data.las
--output Serpent_Mound_Model_LAS_Data.dat
--parse Mxyzirndecaup -v
0,289814.15,4320978.61,170.76,260,0,6,0,0,2,,,32760
1,289814.64,4320978.84,170.76,280,0,6,0,0,2,,,32760
2,289815.12,4320979.06,170.75,280,0,6,0,0,2,,,32760
3,289815.60,4320979.28,170.74,280,0,6,0,0,2,,,32760
...

## Slide 98: Load the Text File into a Point Table
Input table is a text file
Load using SQL*Loader
CREATE TABLE input_points (
rid VARCHAR2(40),
val_d1 NUMBER,
val_d2 NUMBER,
val_d3 NUMBER
)
-73.999922, 40.000002, 74
-73.999921, 40.000002, 27
-73.999920, 40.000002, 76
-73.999919, 40.000002, 72
-73.999918, 40.000002, 91
-73.999917, 40.000002, 96
LOAD DATA
TRUNCATE
INTO TABLE input_points
FIELDS TERMINATED BY ',' (
rid sequence,
val_d1,
val_d2,
val_d3
)
sqlldr scott/tiger
control=point_table.ctl
data=input_points.dat
direct=true
columnarrayrows=20000
streamsize=2560000
multithreading=true

## Slide 99: Initialize the Point Cloud
Define the structure and organization of the point cloud
  Resolution, dimensions, extent
  Block capacity
Specify the location of the blocks for each point cloud
  Name of the point blocks table
The unique identifier of the point cloud is automatically generated.
INSERT INTO LIDAR_SCENES (ID, POINT_CLOUD)
VALUES (
101,
SDO_PC_PKG.INIT(
BASETABLE => 'LIDAR_SCENES',
BASECOL => 'POINT_CLOUD',
BLKTABLE => 'PC_BLK_01',
PTN_PARAMS => 'BLK_CAPACITY=10000',
PC_TOL => 0.05,
PC_TOT_DIMENSIONS => 3,
PC_EXTENT =>
SDO_GEOMETRY (2003, 32617, NULL,
SDO_ELEM_INFO_ARRAY (1,1003,3),
SDO_ORDINATE_ARRAY (
289021, 4320940, 290106, 4323640
)
)
)
);

## Slide 100: Load the Point Cloud from the Point Table
Load a point cloud from a flat table
Structure of the input table
DECLARE
PC SDO_PC;
BEGIN
SELECT POINT_CLOUD INTO PC
FROM LIDAR_SCENES WHERE SCENE_ID = 1;
SDO_PC_PKG.CREATE_PC (PC, 'INPUT_POINTS');
END;
/
RID VARCHAR2(40)
VAL_D1 NUMBER
VAL_D2 NUMBER
…
VAL_Dn NUMBER
Unique point identifier
Point coordinates
Notes
This needs the CREATE VIEW right
Repeating the operation on the same point cloud object will APPEND the new data (not replace it!)

## Slide 101: 5. Create Spatial Indexes
Index on the scenes
INSERT INTO user_sdo_geom_metadata (
table_name, column_name, diminfo, srid)
VALUES (
'LIDAR_SCENES',
'POINT_CLOUD.PC_EXTENT',
sdo_dim_array(
sdo_dim_element('Easting', 200000, 300000, 0.05),
sdo_dim_element('Northing', 4300000, 4400000, 0.05)
),
32617
);
CREATE INDEX lidar_scenes_sx
ON lidar_scenes (point_cloud.pc_extent)
INDEXTYPE IS MDSYS.SPATIAL_INDEX;

## Slide 102: Create Spatial Indexes
Index on the point cloud blocks
INSERT INTO user_sdo_geom_metadata (
table_name, column_name, diminfo, srid)
VALUES (
'PC_BLK_01',
'BLK_EXTENT',
sdo_dim_array(
sdo_dim_element('Easting', 200000, 300000, 0.05),
sdo_dim_element('Northing', 4300000, 4400000, 0.05)
),
32617
);
CREATE INDEX pc_blk_01_sx
ON pc_blk_01 (blk_extent)
INDEXTYPE IS MDSYS.SPATIAL_INDEX;
Note
SDO_PC_PKG.CREATE_PC () automatically creates this index

## Slide 103: 6. Processing Point Clouds
Select scenes using spatial operators
  SDO_PC. PC_EXTENT has the extent of each scene
  SDO_ANYINTERACT, SDO_NN, SDO_FILTER, …
Clip from a scene using a geometric window
Convert to regular geometries
Can also use spatial operators to search through point blocks
  SDO_PC_BLK. BLK_EXTENT has the extent of each block

## Slide 104: Processing Point Clouds
CLIP_PC
  Clip Point Cloud
  2D or 3D query window
  Returns points for any block whose extent intersects the query window
  Only points that intersect the query window are returned
  Creates a set of PC blocks, can be stored or used in queries
TO_GEOMETRY
  Converts the points from a PC block into a multi-point geometry.
  Can be from a CLIP_PC operation

## Slide 105: CLIP_PC: Clipping from a Point Cloud
Selects points from a point cloud that are within a spatial window.
Can also select points based on specific dimension values
Results in an array of point blocks
DECLARE
clip_window SDO_GEOMETRY;
BEGIN
-- Get the clipping window
SELECT geom
INTO clip_window
FROM us_parks
WHERE name = 'Serpent Mound State Memorial';
-- Find the matching scenes
FOR s IN (
SELECT point_cloud
FROM lidar_scenes s
WHERE sdo_anyinteract(
s.point_cloud.pc_extent, clip_window) = 'TRUE'
)
LOOP
-- Clip out the desired subset from the scene
INSERT INTO clipped_lidar_scenes_blocks
SELECT * FROM TABLE (
sdo_pc_pkg.clip_pc (
INP => s.point_cloud,
IND_DIM_QRY => clip_window,
OTHER_DIM_QRY => null,
QRY_MIN_RES => null,
QRY_MAX_RES => null
)
);
END LOOP;
END;
Clip the points that intersect “Serpent Mound State Memorial Park”

## Slide 106: Clipping Result
Clip the points that intersect “Serpent Mound State Memorial Park”
Input
Result

## Slide 107: Clipping from a Point Cloud
The clipping window can be in any coordinate system
Will automatically be transformed to the coordinate system of the points
DECLARE
clip_window SDO_GEOMETRY;
BEGIN
-- Construct the clipping window
clip_window := sdo_geom.sdo_buffer (
SDO_GEOMETRY(2001, 4326,
SDO_POINT_TYPE(-83.430895, 39.0243455, NULL),
NULL, NULL),
200, 0.05, 'UNIT=METER'
);
-- Find the matching scenes
FOR s IN (
SELECT point_cloud
FROM lidar_scenes s
WHERE sdo_anyinteract(
s.point_cloud.pc_extent, clip_window) = 'TRUE'
)
LOOP
-- Clip out the desired subset from the scene
INSERT INTO clipped_lidar_scenes_blocks
SELECT * FROM TABLE (
sdo_pc_pkg.clip_pc (
INP => s.point_cloud,
IND_DIM_QRY => clip_window,
OTHER_DIM_QRY => null,
QRY_MIN_RES => null,
QRY_MAX_RES => null
)
);
END LOOP;
END;
Clip a 200 meter buffer around a point

## Slide 108: Clipping Result
Clip a 200 meter buffer around a point
Input
Result

## Slide 109: TO_GEOMETRY: Convert to Geometries
Extracts the points from a point cloud block
Convert to a multi-point SDO_GEOMETRY object
Can optionally extract the identifiers of the points
NOTES:
Must specify the correct dimensionality for the points BLOB!
CREATE TABLE clipped_lidar_scenes_geom (
obj_id NUMBER,
blk_id NUMBER,
num_points NUMBER,
points SDO_GEOMETRY,
);
INSERT INTO clipped_lidar_scenes_geom
SELECT obj_id, blk_id, num_points,
sdo_pc_pkg.to_geometry (
points, -- LOB containing the points
num_points, -- # of points in the LOB
5, -- Dimensionality of the points
32617 -- SRID for the point cloud
)
FROM clipped_lidar_scenes_blocks;

## Slide 110: TO_GEOMETRY result
The geometry has 5 dimensions!
Points are ordered by their ID
SDO_GEOMETRY( 5005, 32617, NULL,
SDO_ELEM_INFO_ARRAY(1, 1, 9985),
SDO_ORDINATE_ARRAY(
289293.07, 4323470.18, 180.28, 499919.445, 2,
289293.57, 4323470.25, 180.44, 499919.445, 2,
289331.77, 4323386.45, 202.53, 499921.132, 2,
289331.25, 4323386.37, 202.59, 499921.132, 2
)
)
X
Y
Z
Intensity
Time

## Slide 111: TO_GEOMETRY result with point IDs
The geometry has 7 dimensions!
Points are ordered by their ID
SDO_GEOMETRY( 7005, 32617, NULL,
SDO_ELEM_INFO_ARRAY(1, 1, 9985),
SDO_ORDINATE_ARRAY(
289293.07, 4323470.18, 180.28, 499919.445, 2, 319, 946093,
289293.57, 4323470.25, 180.44, 499919.445, 2, 319, 946094,
289331.77, 4323386.45, 202.53, 499921.132, 2, 319, 1030212,
289331.25, 4323386.37, 202.59, 499921.132, 2, 319, 1030213
)
)
X
Y
Z
Intensity
Time
Point ID
Block ID

## Slide 112: Viewing the Points
Must first convert the geometries to valid 3D points!
Use a custom function to remove the additional dimensions
Setup spatial metadata and index
UPDATE clipped_lidar_scenes_geom SET points = remove_attributes (points) ;
insert into user_sdo_geom_metadata (table_name, column_name, diminfo, srid)
values (
'CLIPPED_LIDAR_SCENES_GEOM', POINTS',
sdo_dim_array(
sdo_dim_element('Easting', 200000, 300000, 0.05),
sdo_dim_element('Northing', 4300000, 4400000, 0.05),
sdo_dim_element('Elevation', -10000, 10000, 0.05)
),
32617
);
CREATE INDEX clipped_lidar_scenes_geom ON clipped_lidar_scenes_geom (points)
indextype is MDSYS.SPATIAL_INDEX;

## Slide 113: The REMOVE_ATTRIBUTES function
create or replace function remove_attributes (geom_in sdo_geometry, new_dim number := 3)
return sdo_geometry
is
geom_out sdo_geometry;
dimension number;
num_points number;
i number; j number; k number;
begin
dimension := geom_in.get_dims();
num_points := geom_in.sdo_ordinates.count / dimension;
geom_out := sdo_geometry (
new_dimension*1000+5, -- SDO_GTYPE: 2 or 3D multi-point (2005 or 3005)
geom_in.sdo_srid, -- SDO_SRID: same as input
null, -- SDO_POINT: not used
geom_in.sdo_elem_info, -- SDO_ELEM_INFO: same as input
sdo_ordinate_array() -- SDO_ORDINATES: empty
);
geom_out.sdo_ordinates.extend(new_dimension * num_points);
j := 0; k := 0;
for i in 1..num_points loop
geom_out.sdo_ordinates (j+1) := geom_in.sdo_ordinates (k+1); -- Copy X
geom_out.sdo_ordinates (j+2) := geom_in.sdo_ordinates (k+2); -- Copy Y
geom_out.sdo_ordinates (j+3) := geom_in.sdo_ordinates (k+3); -- Copy Z
j := j + new_dim; k := k + dimension;
end loop;
return geom_out;
end;
/
Copy points from old to new geometry, retaining only the first three dimensions (X, Y and Z)

## Slide 114: Viewing the Points

## Slide 115: Storage Model (2): Simple Point Tables
“Back to basics… a simple flat relational model
X, Y, Z and other attributes stored as ordinary columns
No indexes needed
HCC compression, for extremely high compression rates
Parallel Enabled Smart Scan for extreme performance, including spatial queries.
Takes advantage of intelligent Exadata storage servers
CREATE TABLE points (
x NUMBER,
y NUMBER,
z NUMBER,
intensity NUMBER,
returnval NUMBER,
red NUMBER,
green NUMBER,
blue NUMBER
);

## Slide 116: Point Clouds Workflow for Relational Type
Query and Clip
Convert to Geometries
Generate Elevation Contour Lines
LiDAR Files
Copy
LiDAR Files
LiDAR Files
Flat files
Point tables
Flat files
Flat files
Copy
Direct load from flat ASCII files
Direct load from LAS files

## Slide 117: Loading: Simple and Direct
Define flat files and LAS files as external tables
Pre-processor extracts points from LAS files
Loading is a simple data copy from the external table to the point table
LiDAR Files
Copy
LiDAR Files
LiDAR Files
Flat files
Point tables
Flat files
Flat files
Copy
CREATE TABLE points
NOLOGGING
COMPRESS FOR QUERY HIGH
PARALLEL 96
AS
SELECT x,y,z, intensity, returnval,
red, green, blue
FROM points_las_ext;

## Slide 118: External Table Definition for CSV input
CREATE TABLE points_csv_ext (
x NUMBER,
y NUMBER,
z NUMBER,
intensity NUMBER,
returnval NUMBER,
red NUMBER,
green NUMBER,
blue NUMBER
)
ORGANIZATION EXTERNAL (
TYPE ORACLE_LOADER
DEFAULT DIRECTORY las_data_dir
ACCESS PARAMETERS (
RECORDS DELIMITED BY NEWLINE
FIELDS TERMINATED BY ",")
LOCATION (
'lidar_data_01.dat',
'lidar_data_02.dat’
)
)
REJECT LIMIT UNLIMITED;
Any number of input files

## Slide 119: External Table Definition for LAS input
CREATE TABLE points_las_ext (
x NUMBER,
y NUMBER,
z NUMBER,
intensity NUMBER,
returnval NUMBER,
red NUMBER,
green NUMBER,
blue NUMBER
)
ORGANIZATION EXTERNAL (
TYPE ORACLE_LOADER
DEFAULT DIRECTORY las_data_dir
ACCESS PARAMETERS (
PREPROCESSOR 'preprocessor.sh'
RECORDS DELIMITED BY NEWLINE
FIELDS TERMINATED BY ",")
LOCATION (
'lidar_data_01.las',
'lidar_data_02.las’
)
)
REJECT LIMIT UNLIMITED;
Any number of input files
Filter for LAS data

## Slide 120: Point Cloud tools
libLAS (http://liblas.org/)
  Conversion tools, including las2oci
LAStools (http://rapidlasso.com)
  Maintained by Martin Isenburg, rapidlasso GmbH
  Built on LASlib.
  Rich set of processing tools: clip, merge, classify, grid, tile, …
  Conversion tools: las to DEM, tin, shape, …
  Simple viewer and simple gui
See http://liblas.org/lastools.html for details on the relationship between libLAS and LAStools

## Slide 121: Point Cloud tools
PDAL (http://pointcloud.org/)
  Point Data Abstraction Library, analogous to GDAL
  Data transformation and data access
  Abstract processing from storage
  Version 1.0 released
http://www.laszip.org has pointers to many sources of public LiDAR data

## Slide 122
<Insert Picture Here>
Triangulated Irregular Networks (TINs)

## Slide 123: Triangulated Irregular Networks (TINs)
Representation of surfaces / terrains
Contains a network of irregularly placed triangles
Each point (triangle node) has X, Y and Z coordinates
Node No | X | Y | Z
1 | 15.33 | 6.32 | 3.5
2 | 30.25 | 6.65 | 5.2
3 | 10.43 | 5.19 | 6.1
4 | 14.65 | 9.72 | 4.0
5 | 16.53 | 5.36 | 3.6
6 | 21.22 | 2.23 | 2.3
: | : | : | :
Triangle No | Node 1 | Node 2 | Node 3
1 | 5 | 6 | 3
2 | 3 | 6 | 5
3 | 1 | 5 | 6
: | : | : | :

## Slide 124: Storage Model
Separates logical from physical structures
Logical structures
  Tables containing an SDO_TIN column
  Contains metadata and footprint
  Also contains a pointer to a TIN block table
Physical structures
  “Block tables”
  Contain points and triangles
  Can be very large
  Structure defined in SDO_TIN_BLK object type

## Slide 125: Storage Model
tin 1
tin 2
tin 3
tin 4
TIN table
tin 1 blocks
tin 2 blocks
TIN blocks table
tin 3 blocks
tin 4 blocks
tin 5 blocks
tin 6 blocks
tin 5
tin 6

## Slide 126: Storage Model
tin 1
tin 2
tin 3
tin 4
TIN table
tin 1 blocks
tin 2 blocks
TIN blocks table 1
tin 3 blocks
tin 4 blocks
tin 5 blocks
tin 6 blocks
tin 5
tin 6
TIN blocks table 2

## Slide 127: Storage Model
tin 1
tin 2
tin 3
tin 4
TIN table 1
tin 1 blocks
tin 2 blocks
TIN blocks table
tin 3 blocks
tin 4 blocks
tin 5 blocks
tin 6 blocks
tin 5
tin 6
TIN table 2

## Slide 128: TINs Workflow
TIN tables
Point tables
LiDAR Files
Point loader
LiDAR Files
Flat Files
Load flat ASCII files into point tables …
… then build the TINs from the point tables
Query and Clip
Convert to Geometries
Build from point tables
Generate DEM
Project 2D geometry on TIN

## Slide 129: Package SDO_TIN_PKG
Initialization of a TIN
  sdo_tin_pkg.init()
Loading a TIN from a point cloud
  sdo_tin_pkg.create_tin()
Extracting triangles in a spatial window
  sdo_tin_pkg.clip_tin()
Converting to SDO_GEOMETRY
  sdo_tin_pkg. to_geometry()

## Slide 130: 1. Creating TIN Tables
Use the SDO_TIN type
Can have any number of TIN tables
Include any combination of attributes
Scenes can be searched on any attribute
Also the spatial extent of the scene
CREATE TABLE TINS (
ID NUMBER PRIMARY KEY,
COLLECTION_TS TIMESTAMP,
DESCRIPTION CLOB,
... (any number of attributes) ...
TIN SDO_TIN
);

## Slide 131: The SDO_TIN type
TIN_EXTENT is the footprint of the TIN
May need a spatial index
BASE_TABLE VARCHAR2(70)
BASE_TABLE_COL VARCHAR2(1024)
TIN_ID NUMBER
BLK_TABLE VARCHAR2(70)
PTN_PARAMS VARCHAR2(1024)
TIN_EXTENT MDSYS.SDO_GEOMETRY
TIN_TOL NUMBER
TIN_TOT_DIMENSIONS NUMBER
TIN_DOMAIN MDSYS.SDO_ORGSCL_TYPE
TIN_BREAK_LINES MDSYS.SDO_GEOMETRY
TIN_STOP_LINES MDSYS.SDO_GEOMETRY
TIN_VOID_RGNS MDSYS.SDO_GEOMETRY
TIN_VAL_ATTR_TABLES MDSYS.SDO_STRING_ARRAY
TIN_OTHER_ATTRS SYS.XMLTYPE
TIN table and column
Block table and column

## Slide 132: The SDO_TIN type
Attribute | Explanation
BASE_TABLE | Name of the base table containing a column of type SDO_TIN
BASE_TABLE_COL | Name of the column of type SDO_TIN in the base table
TIN_ID | ID number for the TIN
BLK_TABLE | Name of the table that contains information about each block in the TIN.
PTN_PARAMS | Parameters for partitioning the TIN
TIN_EXTENT | SDO_GEOMETRY object representing the spatial extent of the TIN (the minimum bounding object enclosing all objects in the TIN)
TIN_TOL | Tolerance value for points in the TIN.
TIN_TOT_DIMENSIONS | Total number of dimensions in the TIN. Includes spatial dimensions and any nonspatial dimensions, up to a maximum total of 9.
TIN_DOMAIN | (Not currently used)
TIN_BREAK_LINES | (Not currently used)
TIN_STOP_LINES | (Not currently used)
TIN_VOID_REGIONS | (Not currently used)
TIN_VAL_ATTR_TABLES | SDO_STRING_ARRAY object specifying the names of any value attribute tables for the TIN
TIN_OTHER_ATTRS | XMLTYPE object specifying any other attributes of the TIN

## Slide 133: 2. Creating TIN Block Tables
Using the SDO_TIN_BLK type
Define a primary key on the object and block ids
Use SECUREFILE lobs (new structure in 11g)
Allows compression of the LOBs!
  (also encryption and de-duplication)
CREATE TABLE TIN_BLOCKS_01 OF SDO_TIN_BLK (
PRIMARY KEY (OBJ_ID, BLK_ID)
)
LOB(POINTS)
STORE AS SECUREFILE (COMPRESS HIGH NOCACHE NOLOGGING)
LOB(TRIANGLES)
STORE AS SECUREFILE (COMPRESS HIGH NOCACHE NOLOGGING);

## Slide 134: The SDO_TIN_BLK type
Describes one TIN block
Contains a LOB with the points in that block.
Contains another LOB with the triangles.
OBJ_ID NUMBER
BLK_ID NUMBER
BLK_EXTENT MDSYS.SDO_GEOMETRY
BLK_DOMAIN MDSYS.SDO_ORGSCL_TYPE
PCBLK_MIN_RES NUMBER
PCBLK_MAX_RES NUMBER
NUM_POINTS NUMBER
NUM_UNSORTED_POINTS NUMBER
PT_SORT_DIM NUMBER
POINTS BLOB
TR_LVL NUMBER
TR_RES NUMBER
NUM_TRIANGLES NUMBER
TR_SORT_DIM NUMBER
TRIANGLES BLOB

## Slide 135: The SDO_TIN_BLK type
Attribute | Explanation
OBJ_ID | ID number of the TIN object
BLK_ID | ID number of the block.
BLK_EXTENT | Spatial extent of the block.
BLK_DOMAIN | (Not currently used.)
PCBLK_MIN_RES | Minimum resolution level at which the block is visible in a query. The block is retrieved only if the query window intersects the spatial extent of the block and if the minimum - maximum resolution interval of the query. Usually, lower values mean farther from the view point, and higher values mean closer to the view point.
PCBLK_MAX_RES | Maximum resolution level at which the block is visible in a query.
NUM_POINTS | Total number of points in the POINTS BLOB
NUM_UNSORTED_POINTS | Number of unsorted points in the POINTS BLOB
PT_SORT_DIM | Number of the dimension (1 for the first dimension, 2 for the second dimension, etc) on which the points are sorted.
POINTS | BLOB containing the points.
TR_LVL | (Not currently used.)
TR_RES | (Not currently used.)
NUM_TRIANGLES | Number of triangles in the TRIANGLES BLOB
TR_SORT_DIM | (Not currently used.)
TRIANGLES | BLOB containing the triangles

## Slide 136: Tin BLOB Structures
The POINTS blob contains an array of points
Each point encoded as
  <d> 64-bit floating point numbers (d = the dimensionality of the point)
  One 32 bit integer representing the point number
  One 32 bit integer representing the partition (block) number
The TRIANGLE blob contains an array of triangles
Each triangle defined by 3 points
Each points is identified by a block identifier and a point identifier (both are 32 bit integers).

## Slide 137: 3. Creating TINS
The input is a flat point table just like the one used for creating point clouds
Table can be populated from a text file
Text file can be produced from a LAS file
Structure of the point table:
RID VARCHAR2(40)
VAL_D1 NUMBER
VAL_D2 NUMBER
…
VAL_Dn NUMBER
Unique point identifier
Point coordinates

## Slide 138: Convert LAS file to text
The input is a comma-separated-values (csv) file structure
You can create one from a las file using las2txt
Can choose the format of the output (precision, separator, content)
Can apply various filters and transformations
las2txt –i Serpent_Mound_Model_LAS_Data.las
-o Serpent_Mound_Model_LAS_Data.dat -v
289814.15,4320978.61,170.76
289814.64,4320978.84,170.76
289815.12,4320979.06,170.75
289815.60,4320979.28,170.74
...

## Slide 139: Load the Text File into a Point Table
Input table is a text file
Load using SQL*Loader
CREATE TABLE input_points (
rid VARCHAR2(40),
val_d1 NUMBER,
val_d2 NUMBER,
val_d3 NUMBER
)
-73.999922, 40.000002, 74
-73.999921, 40.000002, 27
-73.999920, 40.000002, 76
-73.999919, 40.000002, 72
-73.999918, 40.000002, 91
-73.999917, 40.000002, 96
LOAD DATA
TRUNCATE
INTO TABLE input_points
FIELDS TERMINATED BY ',' (
rid sequence,
val_d1,
val_d2,
val_d3
)
sqlldr scott/tiger
control=point_table.ctl
data=input_points.dat
direct=true
columnarrayrows=20000
streamsize=2560000
multithreading=true

## Slide 140: Initialize the TIN
Define the structure and organization of the TIN
  Resolution, dimensions, extent
  Block capacity (in points)
Specify the location of the blocks for each TIN
  Name of the TIN blocks table
  Unique identifier in that table
Specify processing parameters
  Stop lines
INSERT INTO TINS(ID, TIN)
VALUES (
1,
SDO_TIN_PKG.INIT(
BASETABLE => 'TINS',
BASECOL => 'TIN',
BLKTABLE => 'TIN_BLK_01',
PTN_PARAMS => 'BLK_CAPACITY=10000',
TIN_TOL => 0.05,
TIN_TOT_DIMENSIONS => 3,
PC_EXTENT =>
SDO_GEOMETRY (2003, 32617, NULL,
SDO_ELEM_INFO_ARRAY (1,1003,3),
SDO_ORDINATE_ARRAY (
289021, 4320940, 290106, 4323640
)
)
)
);

## Slide 141: Load the TIN from the Point Table
Generate the TIN from the point table
Structure of the input table
DECLARE
TIN SDO_TIN;
BEGIN
SELECT TIN INTO TIN
FROM TINS WHERE ID = 1;
SDO_TIN_PKG.CREATE_TIN (TIN, 'INPUT_POINTS');
END;
/
RID VARCHAR2(40)
VAL_D1 NUMBER
VAL_D2 NUMBER
…
VAL_Dn NUMBER
Unique point identifier
Point coordinates

## Slide 142: 5. Create Spatial Indexes
Index on the TINs
INSERT INTO user_sdo_geom_metadata (
table_name, column_name, diminfo, srid)
VALUES (
'TINS',
'TIN.TIN_EXTENT',
sdo_dim_array(
sdo_dim_element('Easting', 200000, 300000, 0.05),
sdo_dim_element('Northing', 4300000, 4400000, 0.05)
),
32617
);
CREATE INDEX tins_sx
ON tins (tins.tin_extent)
INDEXTYPE IS MDSYS.SPATIAL_INDEX;

## Slide 143: Create Spatial Indexes
Index on the TIN blocks
INSERT INTO user_sdo_geom_metadata (
table_name, column_name, diminfo, srid)
VALUES (
‘TIN_BLK_01',
'BLK_EXTENT',
sdo_dim_array(
sdo_dim_element('Easting', 200000, 300000, 0.05),
sdo_dim_element('Northing', 4300000, 4400000, 0.05)
),
32617
);
CREATE INDEX tin_blk_01_sx
ON tin_blk_01 (blk_extent)
INDEXTYPE IS MDSYS.SPATIAL_INDEX;
Note
SDO_TIN_PKG.CREATE_TIN () automatically creates this index

## Slide 144: 6. Processing Tins
Select tins using spatial operators
  SDO_TIN. TIN_EXTENT has the extent of each scene
  SDO_ANYINTERACT, SDO_NN, SDO_FILTER, …
Clip from a scene using a geometric window
Convert to regular geometries
Can also use spatial operators to search through point blocks
  SDO_TIN_BLK. BLK_EXTENT has the extent of each block

## Slide 145: Processing Point Clouds
CLIP_TIN
  Clip a section from a TIN
  2D or 3D query window
  Returns triangles for any block whose extent intersects the query window
  Only triangles that intersect the query window are returned
  Creates a set of TIN blocks, can be stored or used in queries
TO_GEOMETRY
  Gets the triangles (as a 3D surface) from a TIN
  Can be from a CLIP_TIN operation

## Slide 146: CLIP_TIN: Clipping from a TIN
Selects triangles from a tin that are within a spatial window.
Results in an array of tin blocks
The clipping window can be in any coordinate system
The clipping window is automatically transformed to the coordinate system of the TIN.
DECLARE
clip_window SDO_GEOMETRY;
BEGIN
-- Get the clipping window
SELECT geom
INTO clip_window
FROM us_parks
WHERE name = 'Serpent Mound State Memorial';
-- Find the matching tins
FOR s IN (
SELECT tin
FROM tins s
WHERE sdo_anyinteract(
s.tin.tin_extent, clip_window) = 'TRUE'
)
LOOP
-- Clip out the desired subset from the tin
INSERT INTO clipped_tins_blocks
SELECT * FROM TABLE (
sdo_tin_pkg.clip_tin (
INP => s.tin,
QRY => clip_window,
QRY_MIN_RES => null,
QRY_MAX_RES => null
)
);
END LOOP;
Select the triangles that intersect “Serpent Mound State Memorial Park”

## Slide 147: Clipping from a Tin
The clipping window can be in any coordinate system
The clipping window is automatically transformed to the coordinate system of the TIN.
DECLARE
clip_window SDO_GEOMETRY;
BEGIN
-- Construct the clipping window
clip_window := sdo_geom.sdo_buffer (
SDO_GEOMETRY(2001, 4326,
SDO_POINT_TYPE(-83.430895, 39.0243455, NULL),
NULL, NULL),
200, 0.05, 'UNIT=METER'
);
-- Find the matching tins
FOR s IN (
SELECT tin
FROM tins s
WHERE sdo_anyinteract(
s.tin.tin_extent, clip_window) = 'TRUE'
)
LOOP
-- Clip out the desired subset from the tin
INSERT INTO clipped_tins_blocks
SELECT * FROM TABLE (
sdo_tin_pkg.clip_tin (
INP => s.tin,
QRY => clip_window,
QRY_MIN_RES => null,
QRY_MAX_RES => null
)
);
END LOOP;
END;
Select the triangles within a 200 meter buffer around a point

## Slide 148: TO_GEOMETRY: Convert to Geometries
Extracts the triangles from a tin block
Convert to a composite surface SDO_GEOMETRY object
NOTES:
Must specify the correct dimensionality for the points and TIN!
index dimensionality (gtype dim in extent in INIT)
CREATE TABLE clipped_tins_geom (
obj_id NUMBER,
blk_id NUMBER,
num_triangles NUMBER,
triangles SDO_GEOMETRY,
);
INSERT INTO clipped_tins_geom
SELECT obj_id, blk_id, num_triangles,
sdo_tin_pkg.to_geometry (
points, -- LOB with the points
triangles, -- LOB with the triangles
num_points, -- # of points
num_triangles, -- # of triangles
2, -- Dimensionality of the TIN
3, -- Dimensionality of the points
32617 -- SRID of the TIN
)
from clipped_tins_blocks

## Slide 149: TO_GEOMETRY result
The result is a 3D composite surface
One face per triangle
SDO_GEOMETRY(3003, 32617, NULL,
SDO_ELEM_INFO_ARRAY(
1, 1006, 313,
1, 1003, 1,
13, 1003, 1
...,
3745, 1003, 1
),
SDO_ORDINATE_ARRAY(
289917.79, 4322130.29, 203.23,
289914.77, 4322152.71, 201.62,
289917.42, 4322131.4, 203.12,
289917.79, 4322130.29, 203.23,
...
289638, 4323189.34, 183.95,
289410.02, 4323546.61, 174.35,
289409.78, 4323545.32, 174.25,
289638, 4323189.34, 183.95
)
)
First triangle
Last triangle
3D surface

## Slide 150: Viewing the Triangles
Few GIS tools can render a 3D surface.
Split the surface into individual triangles
Use a custom function (GET_ELEMENTS)
CREATE TABLE clipped_tins_geom_split (
obj_id number,
blk_id number,
triangle_id number,
triangle sdo_geometry
);
INSERT into clipped_tins_geom_split
SELECT g.obj_id, g.blk_id, t.element_id, t.element_geom
FROM clipped_tins_geom g, TABLE(get_elements (triangles)) t ;

## Slide 151: The GET_ELEMENTS function
CREATE OR REPLACE FUNCTION get_elements (g sdo_geometry) RETURN sdo_geometry_table
PIPELINED
AS
num_triangles NUMBER;
triangle SDO_GEOMETRY;
BEGIN
num_triangles := g.sdo_elem_info (3);
FOR i IN 1..num_triangles LOOP
triangle := sdo_geometry (3003, g.sdo_srid, null,
sdo_elem_info_array (1, 1003, 1), sdo_ordinate_array());
triangle.sdo_ordinates.extend(12);
FOR j IN 1..12 LOOP
triangle.sdo_ordinates(j) := g.sdo_ordinates((i-1)*12+j);
END LOOP;
PIPE ROW (sdo_geometry_row (i, triangle));
END LOOP;
END;
/
Use a “pipelined” function to return triangles on the fly as they are selected
CREATE OR REPLACE TYPE sdo_geometry_row AS OBJECT (
element_id number,
element_geom sdo_geometry
);
/
CREATE OR REPLACE TYPE sdo_geometry_table AS TABLE OF sdo_geometry_row;
/

## Slide 152: Viewing the Triangles