## Slide 1
<Insert Picture Here>
2 Concepts

## Slide 2: Concepts
Types of Location Data
Geometric primitives: points, lines, polygons
Spatial Data Model: elements, geometries, layers
Coordinate Systems
Spatial Indexing
Spatial Query Model
Types of Spatial Queries

## Slide 3: Types of Location Data
GIS (mapping) data
CAM data
CAD data

## Slide 4: Geometric Primitive Types
Points (X1, Y1):
  Define a location in X and Y
  Are used to represent point features
  Are often used to track moving objects
  Usage examples include locations of buildings, customers, ATMs, or automobiles
  Can be 2D (X,Y) or 3D (X,Y,Z)
A (Xa, Ya)
X
Y

## Slide 5: Geometric Primitive Types
Line strings (X1, Y1, … Xn, Yn):
  Linear features are represented by a series of connected points.
  Self-crossing lines are supported.
  Lines that close to form a ring have no area.
  They are connected by either straight lines or circular arcs, or a combination
  The boundary of a line string is its end points.
  Usage examples include rivers, roads, cables, pipelines, and other linear features.

## Slide 6: Geometric Primitive Types
Polygons (X1, Y1, … Xn, Yn, X1, Y1):
  They are area features.
  Coordinates must close.
  Interior area can be voided using additional polygons (for example, a polygon with holes).
  Polygons can be composed of straight lines or circular arcs, or a combination.
  A polygon can be an optimized circle or an optimized rectangle.
  Self-crossing polygons are not supported.

## Slide 7: Geometric Primitive Types
Polygons:
  A polygon with no voids is considered an outer ring and must have a counterclockwise rotation.
  Voids (inner rings) are stored with clockwise rotation.
  An outer ring must be followed by all its inner rings.
  A polygon can represent a land parcel, region, park, or any feature with area.

## Slide 8: Geometric Primitive Types
Point
Line string
Compound
line string
Arc line
string
Optimized
polygons
Compound
polygon
Self-crossing
line strings
valid
Polygon
Polygon with one or more holes
Arc
polygon
Self-crossing
polygons not valid

## Slide 9: Common Geometric Errors
« Duplicate » points
Self-crossing polygons
Orientation errors

## Slide 10: Self-Crossing Polygon
bad
good
The polygon boundary crosses itself.
Turn it into a multi polygon

## Slide 11: Self-Touching Polygon (1)
Inner Ring
Outer Ring
bad
good
The polygon touches itself back forming a “crescent”-like shape.
Turn it into a polygon with a void

## Slide 12: Self-Touching Polygon (2)
bad
good
The inner ring touches the outer ring at more than one point.
Turn it into a multi-polygon
Inner Ring
Outer Ring

## Slide 13: Spatial Data Model
Spatial layer
Geometry
Element
Point
Line string
Polygon
……
……
……
……
Geometry
Geometry
Element
Element

## Slide 14: Elements
Basic building blocks of a geometry
Same as geometric primitive types
Element types
  Point
  Line string
  Polygon
Constructed using ordinates
Element 1
Element 2
Element 3
Element 4
Element 5
Element 6
Hawaii, USA

## Slide 15: Geometry
Geometry 1
California
Geometry 2
Texas
Geometry 3
Florida
Geometry 4
Hawaii
Represents a spatial feature
Consists of an ordered set of elements

## Slide 16: Layers
Are geometry columns in a table
Consist of geometries that share a common set of attributes
States layer

## Slide 17: Coordinate Systems
A coordinate system (CS) is a means of assigning coordinates to a location.
  It establishes relationships between sets of coordinates.
All spatial data has an associated coordinate system.

## Slide 18: Coordinate Systems Concepts
There are two types of coordinate systems:
  Georeferenced
    Related to a specific representation of Earth
  Local, or nongeoreferenced
    Not related to any representation of Earth
Georeferenced can be of two types:
  Projected (not longitude/latitude)
  Geodetic (longitude/latitude)

## Slide 19: Projected Coordinate System Concepts
Any two points are connected with a straight line.
  The shortest path between two points is through that line.
There is only one way to connect two points.
A polygon can define only one closed area.

## Slide 20: Geodetic Coordinate System Concepts
Any two points on the Earth’s surface can be connected using an infinite number of lines.
The line that defines the shortest distance connecting two points is called a geodesic.
Consider the two points (180,60) and (0,60)
  The shortest path connecting these two points does not follow the 60-degree latitude line.
  It goes through the North Pole!
(180,60)
(0,60)

## Slide 21: Geodetic Coordinate System Restrictions
Element types not supported
  Circular arcs or elements that include arcs (compound elements)
  Circles
Element type restrictions
  No two adjacent points in a line or polygon can be antipodal (exactly on opposite sides of the Earth).
  No polygon element with area equal to or greater than half the area of the Earth.

## Slide 22: Whole Earth Geometry Model
Geodetic coordinates allow geometries that span the 180 degree meridian and poles.
The Whole Earth geometry model requires coordinate system bounds to be (–180 to 180), (–90 to 90).

## Slide 23: What Coordinate System to Use ?
Geodetic CS are the natural choice for large problems (those where no single projected system can give accurate results).
The generality of geodetic solutions is often useful, even for small problems.
The most accurate results for small problems are obtained with a suitable projected CS.
In a spatial column, all geometries must be in the SAME coordinate system !

## Slide 24: Spatial Indexing
R-tree Indexing:
  It is based on minimum bounding rectangles (MBR).
  It indexes two, three, or four dimensions.
Provides an exclusive and exhaustive coverage of spatial objects
Indexes all elements within a geometry including points, lines, and polygons
In 12.1 and before, a spatial index is REQUIRED (mandatory) for spatial queries
In 12.2 and later, the spatial index is OPTIONAL but should be defined for achieving adequate performance

## Slide 25: Spatial Query Model
Layer
Data
Spatial Column
Spatial function
determines
Exact result
Secondary
Filter
Spatial
Functions
Reduced
Data
Set
Index retrieves area of interest
Primary
Filter
Spatial
Index
Exact
Result
Anatomy of a spatial query

## Slide 26: Spatial Query Model
Layer
Data
Spatial Column
Spatial function
determines
Exact result
Secondary
Filter
Spatial
Functions
Exact
Result
Reduced
Data
Set
Exact
Result
Index retrieves area of interest
Primary
Filter
Spatial
Index
Anatomy of a spatial query with internal optimizations

## Slide 27: Primary and Secondary Filter: Example
Which of the pipelines have some interaction with this protected area ?
  Primary filter compares geometry approximations, so the result is not exact.
  Interior optimizations are applied to candidate set.
  Geometry comparisons are done only where required.

## Slide 28: Types of Spatial Queries
Spatial Window Queries
  Find matching spatial objects related to ONE other object
  For example:
    Find all policy holders in the projected path of a hurricane.
    Find all schools less than 50 meters from a mobile phone antenna.
    Find all antennas less than 50 meters from a school
Spatial Join Queries
  Find correlations between two sets of spatial objects
  For example:
    Find all cases where an antenna and a school are less than 50 meters apart