## Slide 1
<Insert Picture Here>
14 Elocation Server

## Slide 2: Elocation Server
Architecture
Installation and configuration
Administration
Notes: Objectives
  This section introduces you to the concepts associated with the Oracle Spatial Routing Engine.

## Slide 3
<Insert Picture Here>
Elocation Architecture

## Slide 4: The Elocation Service
Acts as a dispatcher to Mapviewer, Geocoder and Router.
Provides a single entry point (URL) to all services
Handles all XML requests and forwards them to the proper service
Distributes requests to multiple services for load balancing and high availability
Notes: The Oracle Spatial 10g Routing Engine
  The Oracle Spatial Routing Engine enables the hosting of XML-based Web services that provide the following capabilities:
    Given a route request that consists of a start location and an end location, return route information that can include directions, estimated driving times, and driving distances between the two locations.
    Given a batch route request consisting of a single start location and multiple end locations, returns information that can include estimated driving times, and driving distances between the start node and each of the end nodes.

## Slide 5: Elocation Service Architecture
Router
Geocoder
Mapviewer
eLocation
Client
XML/HTTP
JDBC
Application
Server
Database
Application
Mapviewer
Geocoder
Router
XML/HTTP
Application
Server
Notes: Routing Engine Architecture
  Client applications connect to the Routing Engine and send XML routing requests via the HTTP communications protocol. Requests include information about which database to query, and also information about start and end locations for the route. Start and end locations can be identified either as address information or as the EDGEID, PERCENT, and SIDE attributes resulting from a geocoder request.
  The Oracle Spatial Routing Engine executes in a Java environment, which can be either a middle-tier Java environment or a server Java environment.
  The Routing Engine accepts routing requests, connects to the database using JDBC, fetches information required to process the request, processes the routing request, and sends the results of the routing request back to the requestor.

## Slide 6
<Insert Picture Here>
Installation and Configuration

## Slide 7: Installation and configuration
Deploy ELOCATION.EAR in your application server
  File is in $ORACLE_HOME/md/jlib
Update router configuration
  Manually update file $WEB-INF/config/dispatchercfg.xml
  Or use the admin console at
Restart the elocation application

## Slide 8: Elocation Configuration
Parameters are in “web.xml” file.
Parameters specified as “key/value” pairs
Must restart the elocation application after any change